## Slide 1: Digital Circuits and Logic Design
Chapter 7
Latches, Flip-flops, and Timers

## Slide 2
After this lecture, you should be able to:
Describe operation characteristics of Flip-Flops
Describe applications of Flip-Flops
Implement one-shot and astable multivibrator using 555 timer

## Slide 3: Flip-flops
Flip-Flops Characteristics
Propagation delay time is specified for the rising and falling outputs. It is measured between the 50% level of the clock to the 50% level of the output transition.
50% point on triggering edge
50% point
50% point on LOW-to-HIGH transition of Q
tPLH
tPHL
CLK
CLK
Q
Q
50% point on HIGH-to- LOW transition of Q
The typical propagation delay time for the 74AHC family (CMOS) is 4 ns. Even faster logic is available for specialized applications.

## Slide 4: Flip-flops
Flip-Flops Characteristics
Another propagation delay time specification is the time required for an asynchronous input to cause a change in the output. Again it is measured from the 50% levels. The 74AHC family has specified delay times under 5 ns.
50% point
tPLH
tPHL
Q
50% point
50% point
50% point
Q
PRE
CLR

## Slide 5: Flip-flops
Flip-Flops Characteristics
Set-up time and hold time are times required before and after the clock transition that data must be present to be reliably clocked into the flip-flop.
Setup time is the minimum time for the data to be present before the clock.
Hold time is the minimum time for the data to remain after the clock.
CLK
D
CLK
D
Set-up time, ts
Hold time, tH

## Slide 6: Flip-flops
Flip-Flops Characteristics
Maximum clock frequency
The highest rate at which a flip-flop can be reliably triggered
Minimum pulse widths
Specified by the manufacture for the clock, preset and clear inputs
for various inputs
Power dissipation
The power dissipation is the product of the supply voltage and the average current required.

## Slide 7: Flip-flops
Flip-Flops Applications
Principal flip-flop applications are for temporary data storage, as frequency dividers, and in counters
Typically, for data storage applications, a group of flip-flops are connected to parallel data lines and clocked together. Data is stored until the next clock pulse.
Parallel data input lines
Clock
Clear
Output lines
Q0
Q1
Q2
Q3

## Slide 8: Flip-flops
Flip-Flops Applications
For frequency division, it is simple to use a flip-flop in the toggle mode or to chain a series of toggle flip flops to continue to divide by two.
One flip-flop will divide fin by 2, two flip-flops will divide fin by 4 (and so on). A side benefit of frequency division is that the output has an exact 50% duty cycle.
HIGH
HIGH
CLK
K
J
QA
CLK
K
J
fin
QB
fout
Waveforms:
fin
fout

## Slide 9: Flip-flops
One-Shots (单稳态)
The one-shot or monostable multivibrator is a device with only one stable state. When triggered, it goes to its unstable state for a predetermined length of time, then returns to its stable state.

## Slide 10: Flip-flops
One-Shots
For most one-shots, the length of time in the unstable state (tW) is determined by an external RC circuit.
Trigger
CEXT
REXT
+V
CX
RX/CX
Q
Q
tW
Trigger
Q

## Slide 11: Flip-flops
One-Shots
Nonretriggerable (不可重复触发) one-shots do not respond to any triggers that occur during the unstable state.
Retriggerable one-shots respond to any trigger, even if it occurs in the unstable state. If it occurs during the unstable state, the state is extended by an amount equal to the pulse width.
Retriggerable (可重复触发) one-shot:
Retriggers
tW
Trigger
Q

## Slide 12: Flip-flops
One-Shots
An application for a retriggerable one-shot is a power failure detection circuit. Triggers are derived from the ac power source, and continue to retrigger the one shot. In the event of a power failure, the one-shot is not triggered and an alarm can be initiated.
tW
tW
tW
Retriggers
Retriggers
Triggers derived from ac
Q
Missing trigger due to power failure
Power failure indication

## Slide 13: The 555 timer
The 555 timer

## Slide 14: The 555 timer
The 555 timer
The 555 timer can be configured in various ways, including as a one-shot. A basic one shot is shown. The pulse width is determined by R1C1 and is approximately tW = 1.1R1C1.
The trigger is a negative-going pulse.
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
+VCC
tW = 1.1R1C1
C1
R1

## Slide 15: The 555 timer
The 555 timer

## Slide 16: The 555 timer
The 555 timer

## Slide 17: The 555 timer
The 555 timer
t = RCln([(V1-V0)/(V1-Vt)])

## Slide 18: The 555 timer
The 555 timer
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
+VCC
tW = 1.1R1C1
C1
R1
Determine the pulse width for the circuit shown.
Example
tW = 1.1R1C1 = 1.1(10 kW)(2.2 mF) =
10 kW
2.2 mF
24.2 ms
+15 V

## Slide 19: The 555 timer
Astable Multivibrator
Schmitt Trigger (施密特触发)
A special threshold circuit that produces hysteresis (磁滞)
Prevent erratic switching between states
Allow reliable triggering to occur even when the input is changing slowly

## Slide 20: The 555 timer
The 555 timer
The 555 can be configured as a basic astable multivibrator with the circuit shown. In this circuit C1 charges through R1 and R2 and discharges through only R2. The output frequency is given by:
The frequency and duty cycle are set by these components.
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
C1
R1
R2
+VCC

## Slide 21: The 555 timer
The 555 timer

## Slide 22: The 555 timer
Duty cycle
The period T is
The 555 timer
The time that the output is HIGH(tH) is how long it takes C1 to charge from 1/3 VCC to 2/3 VCC
The time that the output is LOW(tL) is how long it takes C1 to discharge from 2/3 VCC to 1/3 VCC

## Slide 23: The 555 timer
The 555 timer
Given the components, the frequency can be read from the chart. Alternatively, the chart can be used to pick components for a desired frequency.
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
C1
R1
R2
+VCC
C1 (mF)
f (Hz)

## Slide 24: Logic Expression
Logic Expression
S-R flip-flop
Logic Expression
（特性方程）
Truth-table

## Slide 25: Logic Expression
Logic Expression
S-R flip-flop
State Diagram (状态转换图）
Truth-table

## Slide 26: Logic Expression
Logic Expression
D flip-flop
Logic Expression
Truth-table
Qn+1=D
State Diagram

## Slide 27: Logic Expression
Logic Expression
J-K flip-flop
Logic Expression
Truth-table

## Slide 28: Logic Expression
Logic Expression
J-K flip-flop
Truth-table
State Diagram

## Slide 29: Logic Expression
Implement D FF using S-R FF
D flip-flop
S-R flip-flop

## Slide 30: Logic Expression
J-K flip-flop
Implement J-K FF using D FF
CLK
D
CLK
Q
Q
Toggle mode
D flip-flop

## Slide 31: Logic Expression
Implement J-K FF using D FF
J-K flip-flop
D flip-flop

## Slide 32
Quiz
1. The output of a D latch will not change if
a. the output is LOW
b. Enable is not active
c. D is LOW
d. all of the above
2. The D flip-flop shown will
a. set on the next clock pulse
b. reset on the next clock pulse
c. latch on the next clock pulse
d. toggle on the next clock pulse
CLK
D
CLK
Q
Q

## Slide 33
Quiz
3. For the J-K flip-flop shown, the number of inputs that are asynchronous is
a. 1
b. 2
c. 3
d. 4
CLK
K
J
Q
Q
PRE
CLR

## Slide 34
Quiz
4. Assume the output is initially HIGH on a leading edge triggered J-K flip flop. For the inputs shown, the output will go from HIGH to LOW on which clock pulse?
a. 1
b. 2
c. 3
d. 4
CLK
K
J
1 2 3 4

## Slide 35
Quiz
5. The time interval illustrated is called
a. tPHL
b. tPLH
c. set-up time
d. hold time
6. The time interval illustrated is called
a. tPHL
b. tPLH
c. set-up time
d. hold time
50% point on triggering edge
50% point on LOW-to-HIGH transition of Q
CLK
Q
?
CLK
D
?

## Slide 36
Quiz
7. The application illustrated is a
a. astable multivibrator
b. data storage device
c. frequency multiplier
d. frequency divider
HIGH
HIGH
CLK
K
J
QA
CLK
K
J
fin
QB
fout

## Slide 37
Quiz
8. The application illustrated is a
a. astable multivibrator
b. data storage device
c. frequency multiplier
d. frequency divider
Parallel data input lines
Clock
Clear
Output lines
Q0
Q1
Q2
Q3

## Slide 38
Quiz
9. A retriggerable one-shot with an active HIGH output has a pulse width of 20 ms and is triggered from a 60 Hz line. The output will be a
a. series of 16.7 ms pulses
b. series of 20 ms pulses
c. constant LOW
d. constant HIGH
10. The circuit illustrated is a
a. astable multivibrator
b. monostable multivibrator
c. frequency multiplier
d. frequency divider
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
+VCC
C1
R1
R2

## Slide 39: Assignment
Assignment 8 (Due on 28 April 2014)
PP.303
22,24,25,28,30