## Slide 1: Digital Circuits and Logic Design
Chapter 8
Counters

## Slide 2
After this lecture, you should be able to:
Analyze the sequential logics
Identify different types of counters
Implement different types of counters
Design the sequential logics

## Slide 3: Sequential Logic
Sequential Logic
The digital electronic logic is classified as the combinational logic and the sequential logic.
Sequential Logic
Memory Section
Combinational Logic Section

## Slide 4: Sequential Logic
Sequential Logic
The sequential logic is classified as the asynchronous one and synchronous one (异步时序电路和同步时序电路）.
Synchronous
Events that have a fixed time relationship with each other
Asynchronous
Refers to events that do not have a fixed time relationship
with each other and, generally, do not occur at the same time.

## Slide 5: Sequential Logic
Logic Diagram
Combinational Logic
Memory
x1
xi
y1
yj
q1
ql
z1
zk
Y = F[X,Q]
Z = G[X,Q]
Qn+1 = H[Z,Qn]
Output Exp.
State Exp.
Excitation Exp.

## Slide 6: Sequential Logic
Analysis of the Sequential Logic
Procedure:
Write down the clock and excitation expressions for each FF.
Get their state expressions by replacing the logic expression for the FF with its excitation expression.
3. Write down the output expression.
4. Assume the present state, and analyze the next state, and draw its state diagram/state sequence table or its timing diagram.
5. Determine the logic function of the logic diagram.

## Slide 7: Counters
Analysis of the Sequential Logic
Example
What’s the function of the following logic diagram?

## Slide 8: Counters
Analysis of the Sequential Logic
Example
Write down the clock and excitation expressions for each FF.
2. Get their state expressions by replacing the logic expression for the FF with its excitation expression.

## Slide 9: Counters
Analysis of the Sequential Logic
Example
3.Write down the output expression.
4. Assume the present state, and analyze the next state, and draw its state diagram/state sequence table or its timing diagram .

## Slide 10: Counters
Analysis of the Sequential Logic
Example
CP | Q1 | Q0
0 | 0 | 0
1 | 0 | 1
2 | 1 | 0
3 | 1 | 1
4 | 0 | 0
State Sequence Table

## Slide 11: Counters
Analysis of the Sequential Logic
Example
CP | Q1 | Q0
0 | 0 | 0
1 | 0 | 1
2 | 1 | 0
3 | 1 | 1
4 | 0 | 0
00
01
10
11
State Sequence Table
State Diagram
Q1Q0

## Slide 12: Counters
Analysis of the Sequential Logic
Example
Timing Diagram

## Slide 13: Counters
Analysis of the Sequential Logic
Example
A 2-bit synchronous binary counter
00
01
10
11

## Slide 14: Counters
Synchronous Counters
In a synchronous counter all flip-flops are clocked together with a common clock pulse.
The binary count sequence follows a pattern of 0’s and 1’s.
LSB changes on every number.
The next bit changes on every other number.
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
The next bit changes on every fourth number.

## Slide 15: Counters
Counting in Binary
A counter can form the same pattern of 0’s and 1’s with logic levels. The first stage in the counter represents the least significant bit – notice that these waveforms follow the same pattern as counting in binary.
LSB
MSB

## Slide 16: Latches
3-Bit Synchronous Binary Counter
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q0Q1
Q0
Q1
Q2
CLK
HIGH
Example

## Slide 17: Counters
4-bit Synchronous Binary Counter
Q0
Q1
Q2
Q3

## Slide 18: Counters
BCD Decade Counter
With some additional logic, a binary counter can be converted to a BCD synchronous decade counter. After reaching the count 1001, the counter recycles to 0000.
This gate detects 1001, and causes FF3 to toggle on the next clock pulse. FF0 toggles on every clock pulse. Thus, the count starts over at 0000.
Q0
Q3

## Slide 19: Counters
BCD Decade Counter
Waveforms for the decade counter:
CLK
Q0
Q1
Q2
Q3

## Slide 20: Counters
A 4-bit Synchronous Binary Counter
The 74LS163 is a 4-bit IC synchronous counter with additional features over a basic counter. It has parallel load, a CLR input, two chip enables, and a ripple count output that signals when the count has reached the terminal count.
Data inputs
Data outputs
CLR
LOAD
ENT
ENP
CLK
RCO
Q0
Q1
Q2
Q3
D0
D1
D2
D3

## Slide 21: Counters
Data inputs
CLR
LOAD
ENT
ENP
CLK
RCO
Q0
Q1
Q2
Q3
D0
D1
D2
D3
Clear Preset
Count Inhibit
12 13 14 15 0 1 2

## Slide 22: Counters
Up/Down Synchronous Counters
An up/down counter is capable of progressing in either direction depending on a control input.
CLK
Q0
Q1
Q2
K0
J0
C
C
C
J1
J2
K1
K2
HIGH
UP/DOWN
UP
DOWN
FF0
FF1
FF2
Q0.UP
Q0.DOWN
Q0
Q1
Q2

## Slide 23: Counters
Up/Down Synchronous Counters
State Diagram
Q2Q1Q0
000
001
110
111
010
011
100
101
Up sequence
Down sequence

## Slide 24: Counters
Up/Down Synchronous Counters
UP/DOWN
Q0
Q1
Q2
Count up
Count down

## Slide 25: Counters
Up/Down Synchronous Counters
The 74HC191 has the same inputs and outputs but is a synchronous up/down binary counter.
Data inputs
Data outputs
MAX/MIN
CLK
Q0
Q1
Q2
Q3
LOAD
CTEN
RCO
D/U
D0
D1
D2
D3
C
CTR DIV 10
74HC190
Data inputs
Data outputs
MAX/MIN
CLK
Q0
Q1
Q2
Q3
LOAD
CTEN
RCO
D/U
D0
D1
D2
D3
C
CTR DIV 16
74HC191
The 74HC190 is a high speed CMOS synchronous up/down decade counter with parallel load capability. It also has a active LOW ripple clock output (RCO) and a MAX/MIN output when the terminal count is reached.

## Slide 26: Sequential Logics Design
Sequential Logics Design
1. Convert the given problem to a logic problem. Assume the input, output and state variables.
2. Get its state diagram.
3. Get its state sequence table.
4. According to the number of the states, draw a corresponding number-variable K-map.
Procedure:

## Slide 27: Sequential Logics Design
Sequential Logics Design
Procedure:
5. Get the state expressions using K-map.
6. Choose the needed flip-flop.
7.Get the excitation expressions according to the state expressions and logic expression for the corresponding flip-flop.
8. Sketch the logic diagram.

## Slide 28: Sequential Logics Design
Sequential Logics Design
Design a counter with the binary count sequence shown in the state diagram shown below using J-K flip-flops
Example

## Slide 29: Sequential Logics Design
Sequential Logics Design
Example

## Slide 30: Sequential Logics Design
Sequential Logics Design
Example

## Slide 31: Sequential Logics Design
Sequential Logics Design
Example

## Slide 32: Sequential Logics Design
Sequential Logics Design
Example

## Slide 33: Counters
Cascaded counters
HIGH
CLK
Q0
Q1
Q2
C
Counter 1
Counter 2
C
CTEN
CTEN
CTR DIV 16
CTR DIV 16
Q3
Q0
Q1
Q2
Q3
TC
TC
fin
Example
a) Each counter divides the frequency by 16. Thus the modulus is 162 = 256.
Cascading is a method of achieving higher-modulus counters. For synchronous IC counters, the next counter is enabled only when the terminal count of the previous stage is reached.
What is the modulus of the cascaded DIV 16 counters?
If fin =100 kHz, what is fout?
fout
b) The output frequency is 100 kHz/256 = 391 Hz

## Slide 34: Counters
Counter Decoding
Decoding is the detection of a binary number and can be done with an AND gate.
Question
What number is decoded by this gate?

## Slide 35: Counters
Resetting the Count with a Decoder
The divide-by-60 counter also uses partial decoding to clear the tens count when a 6 was detected.
The divide characteristic illustrated here is a good way to obtain a lower frequency using a counter.
For example, the 60 Hz power line can be converted to 1 Hz.

## Slide 36: Counters
Counter Decoding
Show how to decode state 5 with an active LOW output.
Notice that a NAND gate was used to give the active LOW output.
Example

## Slide 37: Counters
Three bit Asynchronous Counter
In an asynchronous counter, the clock is applied only to the first stage. Subsequent stages derive the clock from the previous stage.
The three-bit asynchronous counter shown is typical. It uses J-K flip-flops in the toggle mode.
CLK
K0
J0
Q0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
Q1
HIGH

## Slide 38: Counters
Three bit Asynchronous Counter
Notice that the Q0 output is triggered on the leading edge of the clock signal. The following stage is triggered from Q0. The leading edge of Q0 is equivalent to the trailing edge of Q0. The resulting sequence is that of an 3-bit binary up counter.
CLK
Q0
Q1
Q2

## Slide 39: Counters
Three bit Asynchronous Counter
Asynchronous counters are sometimes called ripple counters, because the stages do not all change together.
For certain applications requiring high clock rates, this is a major disadvantage.
Notice how delays are cumulative as each stage in a counter is clocked later than the previous stage.
CLK
Q0
Q1
Q2
Q0 is delayed by 1 propagation delay, Q2 by 2 delays and Q3 by 3 delays.

## Slide 40: Counters
Asynchronous Decade Counter
This counter uses partial decoding to recycle the count sequence to zero after the 1001 state. The flip-flops are trailing-edge triggered, so clocks are derived from the Q outputs. Other truncated sequences can be obtained using a similar technique.
CLK
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
HIGH
C
J3
K3
Q3
CLR

## Slide 41: Counters
Asynchronous Decade Counter
When Q1 and Q3 are HIGH together, the counter is cleared by a “glitch” on the CLR line.
CLK
Q0
Q1
Q2
Q3
CLR
Glitch
Glitch

## Slide 42: Counters
Asynchronous Counter Using D Flip-flops
D flip-flops can be set to toggle and used as asynchronous counters by connecting Q back to D.

## Slide 43: Counters
Asynchronous Counter Using D Flip-flops
CLR
CLK
LSB
MSB
Note that it is momentarily in state 3 which causes it to clear.
The sequence is 0 – 2 – 1 – (CLR) (repeat)…

## Slide 44: Counters
74LS93A Asynchronous Counter
The 74LS93A has one independent toggle J-K flip-flop driven by CLK A and three toggle J-K flip-flops that form an asynchronous counter driven by CLK B.
The counter can be extended to form a 4-bit counter by connecting Q0 to the CLK B input. Two inputs are provided that clear the count.
CLK A
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
C
J3
K3
Q3
CLK B
RO (1)
RO (2)
All J and K inputs are connected internally HIGH

## Slide 45: Counters
Applications
A Digital Clock
Parking Control

## Slide 46: Counters
Applications
Parallel to Serial Data Conversion

## Slide 47: Assignment
Assignment 9 (Due on 5 May 2014)
PP.355
2,4(a,e),6,9,12,16,18,22(a),24(a),26,