## Slide 1: Digital Circuits and Logic Design
Chapter 9
Shift Register

## Slide 2
After this lecture, you should be able to:
Identify different basic shift register operations
Implement different basic shift registers
Describe applications of shift registers

## Slide 3: Shift Register
Basic Shift Register Functions
Shift registers are a type of sequential logic circuits closely related to digital counters.
Shift registers consist of an arrangement of FF and are important in application involving the storage and transfer of data in a digital system.
It can store and shift data (1s and 0s)entered into it from an external source.

## Slide 4: Shift Register
Basic Shift Register Functions
A register is a digital circuit with two basic functions: data storage and data movement.
The storage capacity of a register is the total number of bits (1s and 0s) of digital data it can retain.
Each state (FF) in a shift register represents one bit of storage capacity; therefore, the number of states in a register determines its storage capacity.

## Slide 5: Shift Register
Basic Shift Register Operations
A shift register is an arrangement of flip-flops with important applications in storage and movement of data. Some basic data movements are illustrated here.
Data in
Data in
Data in
Data in
Data in
Data out
Data out
Data out
Data out
Data out
Serial in/shift right/serial out
Serial in/shift left/serial out
Parallel in/serial out
Parallel in/parallel out
Serial in/parallel out
Rotate right
Rotate left

## Slide 6: Shift Register
Serial-in/Serial out Shift Register
The serial in/serial out shift register accepts data serially- that is, one bit at a time on a single line.
It produces the stored information on its output also in serial form.
1
1
1
1
1
1
CLK
CLK
CLK
CLK
CLK

## Slide 7: Shift Register
Serial-in/Serial out Shift Register

## Slide 8: Shift Register
Serial-in/Parallel out Shift Register
4-bit serial in/parallel out shift register and its logic symbol

## Slide 9: Shift Register
The 74HC164A Shift Register
The 74HC164A is a CMOS 8-bit serial in/parallel out shift register. VCC can be from +2.0 V to +6.0 V.
One of the two serial data inputs may be used as an active HIGH enable to gate the other input. If no enable is needed, the other serial input can be connected to VCC.
The 74HC164A has an active LOW asynchronous clear. Data is entered on the leading-edge of the clock.
CLK
Q0
Q1
Q2
Q3
CLR
Q4
Q5
Q6
Q7
Serial inputs
A
B

## Slide 10: Shift Register
Waveforms for the 74HC164A
CLK
Q0
Q1
Q2
Q3
CLR
Q4
Q5
Q6
Q7
Serial inputs
A
B
Outputs
Clear
Clear
Sample waveforms for the 74HC164A are shown. Notice that B acts as an active HIGH enable for the data on A as discussed.
As with CMOS devices, unused inputs should always be connected to a logic level; unused outputs should be left open.

## Slide 11: Shift Register
Parallel in/Serial out Shift Register

## Slide 12: Shift Register
Parallel in/Serial out Shift Register
Shift registers can be used to convert parallel data to serial form. A logic diagram for this type of register is shown:
D0
D1
D2
D3
Q0
Q1
Q2
Q3
SHIFT/LOAD
CLK
Serial data out

## Slide 13: Shift Register
The 74HC165 Shift Register
The 74HC165 is a CMOS 8-bit parallel in/serial out shift register. The logic symbol is shown:
D0
D1
D2
D3
D4
D5
D6
D7
Q7
Q7
SH/LD
CLK
SER
CLK INH
The clock (CLK) and clock inhibit (CLK INH) lines are connected to a common OR gate, so either of these inputs can be used as an active-LOW clock enable with the other as the clock input.

## Slide 14: Shift Register
The 74HC165 Shift Register
The 74HC165 can also be operated as serial in/serial out.
Data can be entered serially on the SER input.
D0
D1
D2
D3
D4
D5
D6
D7
Q7
Q7
SH/LD
CLK
SER
CLK INH
Data is loaded asynchronously when SH/LD is LOW and moved through the register synchronously when SH/LD is HIGH and a rising clock pulse occurs.

## Slide 15: Shift Register
Parallel in/Parallel out Shift Register

## Slide 16: Shift Register
Bidirectional Shift Register

## Slide 17: Shift Register
Bidirectional Shift Register
Bidirectional shift registers can shift the data in either direction using a RIGHT/LEFT input.

## Slide 18: Shift Register
Bidirectional Shift Register
Bidirectional shift registers can shift the data in either direction using a RIGHT/LEFT input.
CLK
RIGHT/LEFT
Serial data in
Q0
Q1
Q2
Q3
Shift right
Shift left

## Slide 19: Shift Register
Bidirectional Shift Register
CLK
RIGHT/LEFT
Serial data in
Q0
Q1
Q2
Q3
Shift right
Shift left
Question
How will the pattern change if the RIGHT/LEFT control signal is inverted?
Shift right
Shift left

## Slide 20: Shift Register
Universal Shift Register
A universal shift register has both serial and parallel input and output capability.
The 74HC194 is an example of a 4-bit bidirectional universal shift register.
D0
D1
D2
D3
CLK
SL SER
Q0
Q1
Q2
Q3
SR SER
S1
S0
CLR

## Slide 21: Shift Register
Universal Shift Register

## Slide 22: Shift Register Counters
Shift Register Counters
A shift register counter is basically a shift register with the serial output connected back to the serial input to produce special sequences.
There are two most common types of shift register counters:
Johnson counter
Ring counter

## Slide 23: Shift Register Counters
Johnson Counter
In a Johnson counter, the complement of the output of the last flip-flop is connected back to the input of the first flip-flop.

## Slide 24: Shift Register Counters
Johnson Counter
Redrawing the same Johnson counter (without the clock shown) illustrates why it is sometimes called as a “twisted-ring” counter.

## Slide 25: Shift Register Counters
Johnson Counter
The Johnson counter is useful when you need a sequence that changes by only one bit at a time but it has a limited number of states (2n, where n = number of stages).
The first five counts for a 4-bit Johnson counter that is initially cleared are: CLK Q0 Q1 Q2 Q3
0 0 0 0
1 0 0 0
1 1 0 0
1 1 1 0
1 1 1 1
0 1 1 1
0 0 1 1
0 0 0 1
0
1
2
3
4
5
6
7

## Slide 26: Shift Register Counters
Johnson Counter
4-bit Johnson counter

## Slide 27: Shift Register Counters
Johnson Counter
State Diagram
Modulus-2n
It Can’t startup automatically.

## Slide 28: Shift Register Counters
Johnson Counter

## Slide 29: Shift Register Counters
Ring Counter
The ring counter can also be implemented with either D flip-flops or J-K flip-flops.

## Slide 30: Shift Register Counters
Ring Counter
Redrawing the Ring counter (without the clock shown) shows why it is a “ring”.
The disadvantage to this counter is that it must be preloaded with the desired pattern (usually a single 0 or 1) and it has even fewer states than a Johnson counter (n, where n = number of flip-flops).
On the other hand, it has the advantage of being self-decoding with a unique output for each state.

## Slide 31: Shift Register Counters
Ring Counter
4-bit Ring counter

## Slide 32: Shift Register Counters
Ring Counter
State Diagram
Modulus-n
It Can’t startup automatically.
Valid Cycle

## Slide 33: Shift Register Counters
Ring Counter

## Slide 34: Shift Register Counters
Ring Counter
A common pattern for a ring counter is to load it with a single 1 or a single 0. The waveforms shown here are for an 8-bit ring counter with a single 1.

## Slide 35: Applications
Shift Register Applications
Shift registers can be used to delay a digital signal by a predetermined amount.
Example
An 8-bit serial in/serial out shift register has a 40 MHz clock. What is the total delay through the register?
The delay for each clock is 1/40 MHz = 25 ns
The total delay is 8 x 25 ns = 200 ns
25 ns
= 200 ns

## Slide 36: Applications
Shift Register Applications
A UART (Universal Asynchronous Receiver Transmitter) is a serial-to-parallel converter and a parallel to serial converter.
Data bus
Serial data in
Serial data out
CLK
CLK
Start
Bit (0)
Stop Bits (1)

## Slide 37: Applications
Shift Register Applications
The keyboard encoder is an example of where a ring counter is used in a small system to encode a key press.
Two 74HC195 shift registers are connected as an 8-bit ring counter preloaded with a single 0. As the 0 circulate in the ring counter, it “scans” the keyboard looking for any row that has a key closure. When one is found, a corresponding column line is connected to that row line. The combination of the unique column and row lines identifies the key.

## Slide 38: Applications

## Slide 39
Quiz
1. The shift register that would be used to delay serial data by
4 clock periods is
a. c.
b. d.

## Slide 40
Quiz
2. The circuit shown is a
a. serial-in/serial-out shift register
b. serial-in/parallel-out shift register
c. parallel-in/serial-out shift register
d. parallel-in/parallel-out shift register

## Slide 41
Quiz
3. If the SHIFT/LOAD line is HIGH, data
a. is loaded from D0, D1, D2 and D3 immediately
b. is loaded from D0, D1, D2 and D3 on the next CLK
c. shifted from left to right on the next CLK
d. shifted from right to left on the next CLK

## Slide 42
Quiz
4. A 4-bit parallel-in/parallel-out shift register will store data for
a. 1 clock period
b. 2 clock periods
c. 3 clock periods
d. 4 clock periods

## Slide 43
Quiz
5. The 74HC164 (shown) has two serial inputs. If data is placed on the A input, the B input
a. could serve as an active LOW enable
b. could serve as an active HIGH enable
c. should be connected to ground
d. should be left open
CLK
Q0
Q1
Q2
Q3
CLR
Q4
Q5
Q6
Q7
Serial inputs
A
B

## Slide 44
Quiz
6. An advantage of a ring counter over a Johnson counter is that the ring counter
a. has more possible states for a given number of flip-flops
b. is cleared after each cycle
c. allows only one bit to change at a time
is self-decoding
7. A possible sequence for a 4-bit ring counter is
a. … 1111, 1110, 1101 …
b. … 0000, 0001, 0010 …
c. … 0001, 0011, 0111 …
d. … 1000, 0100, 0010 …

## Slide 45
Quiz
8. The circuit shown is a
a. serial-in/parallel-out shift register
b. serial-in/serial-out shift register
c. ring counter
d. Johnson counter

## Slide 46
Quiz
9. Assume serial data is applied to the 8-bit shift register
shown. The clock frequency is 20 MHz. The first data bit
will show up at the output in
a. 50 ns
b. 200 ns
c. 400 ns
d. 800 ns

## Slide 47
Quiz
10. For transmission, data from a UART is sent in
a. asynchronous serial form
b. synchronous parallel form
c. can be either of the above
d. none of the above

## Slide 48: Assignment
Assignment 10 (Due on 19 May 2014)
PP.355
3,4,14