## Slide 1: Proteus Tutorial
Introduction to Proteus

## Slide 2: Proteus
What is Proteus?
  Proteus is one of the most famous simulators
  Can be uses to simulate almost every circuit on electrical fields.
  Easy to use because of the GUI interface that is very similar to the real Prototype board.
  Can be used to design Print Circuit Board (PCB)..

## Slide 3: Getting Started
Start > All Programs > Proteus 8 Professional
  License Manager
  Proteus 8 Professional
  Proteus help

## Slide 4: Create a Project

## Slide 5: Create a Project

## Slide 6: Create a Project
Templates are provided to create schematic

## Slide 7: Create a Project
Templates are provided to create PCB

## Slide 8
Circuit Window
Toolbars
Proteus Interface

## Slide 9
Proteus Tools
Parts Browsing
Proteus has many models of electronic equipment such as logic gates, many kinds of switches and basic electronic devices.
These equipment can be founded by clicking on and then

## Slide 10
Proteus Tools
Parts Browsing

## Slide 11
Proteus Tools
Parts Browsing
Finding Steps:
1. Type information of the device such as “and gate” in the box 1
2. If some specific category is known, the device can narrow on focusing by selecting catalogue in the box 2
3. After the information is put, the list of the related devices will appear in the box 3, so that needed device can be choose here and then click “OK” button to confirm the selection.

## Slide 12
Proteus Tools
Parts Browsing

## Slide 13
Proteus Tools
Power Supplies and input signal generators
All of the input generators, such as ac, dc, and pulse, are contained in this category and it will be shown when are clicked.

## Slide 14
Proteus Tools
Power Supplies and input signal generators
“Ground” will not contain in this groups because it is not input signal but it is just a terminal junction. Therefore it will be group in the terminal ( ) category

## Slide 15
Proteus Tools
Power Supplies and input signal generators
There is another input that usually be used in digital circuit designed system but it does not exist in real world as an equipment. It is called as “LOGIC STATE”.
It can be find in picking part section (typing “logicstate”) and pick it.

## Slide 16
Proteus Simulation
Simulation
Placing Equipment
1. Click on and select a first device that will be placed. Place mouse to wherever the device is preferred to be place and then click the left button of the mouse. The device will be placed.
2. If it is needed to be moved. Click the right button of the mouse on the device symbol to select the part and then hold the left button of the mouse and move the symbol to wherever it is needed to be places

## Slide 17
Proteus Simulation
Simulation
Placing Equipment

## Slide 18
Proteus Simulation
Simulation
Placing Equipment
3. To wire the device together, click at the source pin of the device and then move mouse cursor to the destination pin of the device. In this step the pink line will be appear and it will be the wire of the circuit after click mouse on the destination pin of the circuit.

## Slide 19
Proteus Simulation
Simulation
Placing Equipment

## Slide 20
Proteus Simulation
Simulation
Placing Equipment
4. After wiring all of the devices and all input together, the simulation is ready to be run by clicking on to run and
to stop. However, to see the result measurements needed to be added in the circuit. They will be explained in next part.

## Slide 21
Proteus Simulation
Simulation
Measuring Digital data
The digital result on proteus can be seen in small square at the pin of the equipments and the state will be shown in 4 colors (red = logic “1”, Blue = logic ”0”, Grey = Unreadable logic and Yellow = Logic congestion).
However, proteus build a modules that can be used to show the logic in 2 ways.

## Slide 22
Proteus Simulation
Simulation
Measuring Digital data
Logic display
The display that proteus has for seeing logic value is called “logic-probe”. It has 2 sizes which have the same functions. It can be found from “picking devices” page

## Slide 23
Proteus Simulation
Simulation
Measuring Digital data
2. Waveform display
Proteus creates digital logic analyzer for the high frequency jobs. To use the logic analyzer on proteus following these steps.
a. Click on and place the voltage probe to the point the needed to measure. After connect the probe to measured point, the probe will be named as identifier of the measure point.
b. Click on and select “digital” from “Graphs” box then assign the are of digital display. The Green screen will appear as
measurement monitor.

## Slide 24
Proteus Simulation
Simulation
Measuring Digital data
2. Waveform display

## Slide 25
Proteus Simulation
Simulation
Measuring Digital data
2. Waveform display
c. Clicking at the word “DIGITAL ANALYSIS” on the screen.
New window will appear as the expanded screen

## Slide 26
Proteus Simulation
Simulation
Measuring Digital data
2. Waveform display
d. Click on graph>> add trace, new pop up window will appear to add the measure points needed on “Probe P1” (if many probes appear on the design, proteus may ask to offer all probes adding) then click OK. The select probes will be added on the screen.

## Slide 27
Proteus Simulation
Simulation
Measuring Digital data
2. Waveform display
d.

## Slide 28
Proteus Simulation
Simulation
Measuring Digital data
2. Waveform display
e. To see the result of the design, must be clicked to simulation for 1 second.